## Slide 1
APC • TECHNICAL PRESENTATION
Working of Display Devices
with special reference to Cathode-Ray Tubes (CRTs)
A study of how electronic signals become visible images
Prepared for classroom presentation
01 / 12

## Slide 2
01 — FOUNDATIONS
A display is the interface between data and people
The same digital information can be rendered through very different physical mechanisms.
02 / 12
INPUT
Text • image • video
PROCESSING
Pixel / timing data
DISPLAY
Light is generated or controlled
PERCEPTION
The eye sees an image
Core idea
A display converts a signal into a visual output.
Key distinction
Some displays emit light; others modulate a backlight or reflect ambient light.
Why CRTs matter
CRTs use a moving electron beam and a phosphor-coated screen.

## Slide 3
02 — THE LANDSCAPE
Display devices: different physics, same purpose
A useful comparison begins with how each technology creates the visible image.
03 / 12
CRT
Electron beam excites phosphor
Emissive • bulky • deep blacks
LCD
Liquid crystals control light from a backlight
Light-modulating • thin • efficient
LED display*
LEDs produce the image directly, or backlight an LCD
Bright • scalable • terminology varies
OLED
Organic pixels emit their own light
Thin • high contrast • pixel-level control
E-paper
Reflects ambient light using electrically moved particles
Low power for static pages
*In consumer language, “LED TV/monitor” usually means an LCD panel with LED backlighting.

## Slide 4
03 — CRT ARCHITECTURE
Inside a cathode-ray tube
A CRT is an evacuated glass tube that directs electrons onto a phosphor-coated screen.
04 / 12
Electron gun
Focusing & accelerating anodes
Deflection system
Phosphor screen
Vacuum inside the tube allows electrons to travel with minimal collision with air molecules.

## Slide 5
04 — IMAGE FORMATION
Step 1: generate and shape the electron beam
The electron gun controls the beam current and focuses electrons into a narrow stream.
05 / 12
01
HEATED CATHODE
Releases electrons by thermionic emission.
02
CONTROL GRID
Varies beam current, controlling brightness.
03
ANODES
Accelerate electrons and help focus the beam.
04
FOCUSED BEAM
A narrow stream travels toward the screen.
Brightness is primarily controlled by beam current; acceleration voltage influences electron energy and screen impact.

## Slide 6
05 — SCANNING
Step 2: steer the beam across the screen
Magnetic or electrostatic fields change the beam’s direction so it can address different screen positions.
06 / 12
Raster scan
Horizontal sweep
Moves the beam left to right.
Vertical sweep
Moves the scan from top to bottom.
Blanking
Beam is suppressed during retrace.
Synchronization
Keeps scanning aligned with the signal.
The beam scans repeatedly; changing its intensity during the scan produces the image.

## Slide 7
06 — LIGHT OUTPUT
Step 3: phosphor converts electron energy into visible light
The screen glows when struck by electrons; its persistence determines how quickly the light decays.
07 / 12
MONOCHROME CRT
Brightness varies with beam intensity
COLOUR CRT
Red + green + blue phosphors combine to create colour
A colour CRT uses three electron beams and a shadow mask or aperture grille to direct each beam to its matching phosphor colour.

## Slide 8
07 — THE FULL PROCESS
From electrical signal to a stable picture
A CRT display depends on coordinated control of position, intensity, and timing.
08 / 12
VIDEO SIGNAL
Image brightness / colour data
CONTROL CIRCUITS
Set beam intensity and scan timing
DEFLECTION
Position beam across the screen
PHOSPHOR
Emits light at each addressed point
PERSISTENCE + EYE
Rapid refresh appears continuous
Position + intensity
The scan decides where light appears; the video signal decides how bright each point is.
Refresh + persistence
Repeated scans refresh the picture before the previous image fades noticeably.

## Slide 9
08 — EVALUATION
Why CRTs were valued
CRT strengths followed directly from their electron-beam and phosphor design.
09 / 12
Motion clarity
Fast response and little sample-and-hold blur.
Viewing angles
Image quality remains broadly consistent off-axis.
Native resolution flexibility
Can display multiple resolutions without a fixed pixel grid.
Black level & contrast
A dark screen can emit very little light in unlit areas.
These advantages are context-dependent: image quality also depends on tube design, calibration, and operating conditions.

## Slide 10
09 — LIMITATIONS
Why CRTs were largely replaced
Their physical construction creates trade-offs that modern flat-panel displays largely avoid.
10 / 12
Size & weight
Large glass vacuum tube makes the device deep and heavy.
Power & heat
High-voltage electronics and beam systems consume energy and generate heat.
Geometry
Curved screens can show distortion; convergence and focus need calibration.
Environmental handling
Heavy glass and electronic components require appropriate recycling.
Safety note: CRTs can retain hazardous high voltage even after unplugging; servicing belongs to trained technicians.

## Slide 11
10 — COMPARISON
CRT vs modern flat-panel displays
No technology wins every category; the right choice depends on the use case.
11 / 12
CRITERION
CRT
LCD / LED-LCD
OLED
E-PAPER
Image mechanism
Electron beam + phosphor
Liquid crystal + backlight
Self-emitting pixels
Reflective particles
Form factor
Deep, heavy
Thin, light
Very thin
Thin, light
Motion
Very fast response
Varies by panel
Very fast response
Slow refresh
Power profile
Relatively high
Moderate; varies
Content-dependent
Very low for static pages
Typical role
Legacy / specialist
General-purpose
Premium video / phones
Readers / signage
Performance varies by model; “LED display” can mean direct-view LED or an LCD using LED backlighting.

## Slide 12
11 — CONCLUSION
The key takeaway
CRTs show how a controlled stream of electrons can paint a moving image using light-emitting phosphor.
12 / 12
01
Generate
The electron gun releases, controls, and focuses electrons.
02
Steer
Deflection fields position the beam across the screen.
03
Illuminate
Phosphor emits visible light when struck by electrons.
04
Refresh
Repeated scanning and signal timing maintain the picture.
Final perspective
Although CRTs have mostly given way to flat panels, their operating principle remains a clear example of signal processing, electron physics, and human visual perception working together.
THANK YOU • QUESTIONS
Editable slides • diagrams built from PowerPoint shapes